## Slide 1: Introduction To Writing Signal Processing Applications In Python Using GNURadio
What is it?
What is built with it?
How to build something with it!

## Slide 2: Outline
What is GNURadio
Building a block
Connecting Blocks
Packaging and deploying

## Slide 3: What GNURadio Provides
Framework
  Currently C++ and Python
Development tools
  Tools to packages and interface your code with others
Scheduler
  Use all the cores
Interface and abstraction of hardware
  Both radio and some acceleration
Library of DSP
Graphical interface / GNURadio Companion

## Slide 4: What is GNURadio
Collection of stuff needed for software defined radio
  Also applies to other signal processing applications
  Collection of functions and algorithms
  Standard means of interacting with the outside
  Many of the things you don’t want to write
Things build with GNURadio
  gr-specest
  gr-lte
  gr-radar
  gr-sigmf
  gr-air-modes
  gr-limesdr
  gr-pdu_utils
  gr-satellites
  gr-iio
  gr-doa
  gr-fosphor

## Slide 5: Graphical interface / GNURadio Companion
Most recognized feature of GNURadio
  Maybe least useful
    Just an opinion
Provides graphical means of connection operations
  Color shows type
Makes descriptive graphics
Not used in talk

## Slide 6: Library of DSP
Gr-filter
  Filter stuff
Gr-digital
  Modulation, demodulation
Gr-analog
  AGC, AM, FM...
Gr-fec
  Error correction
Gr-vocoder
  Vocoders
Gr-channel
  Channel simulation
Gr-fft
  FFT
Volk
  Vector optimized library of kernels

## Slide 7: Let's Build a Block
Think of some piece of code you want in a block

## Slide 8: What is a block
Work function
Setup and initialization
Control
User defined methods
User space/code
GNURadio Scheduler
Input
Circular ring FIFO
User space/code
Output
Circular ring FIFO
GNURadio Block

## Slide 9: What is a block
Work function
Setup and initialization
Control
User defined methods
User space/code
GNURadio Scheduler
Input
Circular ring FIFO
User space/code
Output
Circular ring FIFO
GNURadio Block
Your Code Here

## Slide 10: Types of blocks
Sync
  Synchronous, one in one out
Source
  Where the data comes from
Sink
  Where the data goes
Interpolator
  One in many out
Tagged stream
  Labeled in labeled out
General
  Something in maybe something else out
Decimator
  Many in one out
Hier
  Blocks in blocks

## Slide 11: What does a block ​need
What does a block needs
  Setup
    constructor or __init__
  Work
    Code to do the task
  Schedule
    For data in how much comes out
Inherits from base class
Not needed but nice to have
  Graphical description for GRC
    Was XML, +3.8.0 uses YAML
  Works with tags
  Unit testing and profiling
  Version control

## Slide 12: Example Empty Block
form gnuradio import gr
class MyBlock(gr.sync_block):
def __init__(self, *args, **kwargs):
gr.sync_block.__init__(self,
in_sig=[complex],
out_sig=[complex])
# Add constructor stuff
def work(self, input_items, output_items):
in0 = input_items[0]
out = output_items[0]
out[:] = in0
# Add signal processing
Return len(out)
Notes: Talk about how to put code into a block

## Slide 13: Constructor and Initializer
Builds the block
Inherits from one of the block types
  Source, Sink, Sync, Interpolator, Decimator, Tagged stream, Hier
  Must call parent constructor/initializer
Executes once
  Contains user's setup code
def __init__(self, *args, **kwargs):
gr.sync_block.__init__(self,
in_sig=[complex],
out_sig=[complex])
# Add constructor stuff

## Slide 14: Work Function
Where the work happens
Executes are on each buffered chuck of data
  Called multiple times
Maps buffers as input arguments
  input_items, output_items
  Each input is a list of buffers
  Python buffer protocol
  Numpy array
Returns the number of items written to the output buffer
def work(self, input_items, output_items):
in0 = input_items[0]
out = output_items[0]
out[:] = in0
return len(out)

## Slide 15: Building with Blocks
Assembling your application with blocks

## Slide 16: Top block
Provides common interface to a signal processing chain
  How the schedular interacts with your code
Contains all the blocks
Distributes across multiple processes and cores
Graphical tools produce sub-class of top block
Implementation uses inheritance
Provides methods
  Start
    Gets the data moving
  Run
    Gets the data moving and waits for it to finish
  Wait
    Waits for it to finish
  Stop
    Stops the movement of data

## Slide 17: Connecting the blocks
class FlowGraph(gr.top_block):
def __init__(self):
gr.top_block.__init__(self, name="Flow graph")
# Creating the blocks
self.block1 = Block1(...)
self.block2 = Block2(...)
# Connecting the blocks
self.connect((self.block1, 0), (self.block2, 0))
# Connect takes 2 tuples of the block instance and the number

## Slide 18: Note on Types and Vectors
Types
  Complex float 32
  Float 32
  Int 32
  Short 16
  int 8
Vectors
  Vectors of samples
Currently no explicit support for heterogenous types or structures
  easily be worked around

## Slide 19: Starting and Stopping the Process
Starting the top block
  Start method
    None blocking
  Run method
    Blocking
Stopping the top block
  Call the stop method on the top block
  Blocks work functions returns a negative number
  Raise an exception

## Slide 20: Questions ?
Comments
Concerns
Complaints
Accusations
Allegations

## Slide 21: The End
Thank you for your time

## Slide 22: Missing from this talk
Reconfiguration
Packaging and deployment
Tagged streams
Polymorphic types
Vectors
Libraries of existing components
MAC Layer
Proper unit testing
GRC and GUI
Messaging
C++
Building useful things
Hardware
Simulation

## Slide 23: Packaging everything into an OOT
Out Of Tree package

## Slide 24: What is OOT
Standard way of packaging code
  Directory structure
Build tools
  Cmake, make
Testing tools
  Ctest, python nose, CppUnit
Install tools
  Make install

## Slide 25: General Structure of an OOT’s
Directories
  ./apps/
  ./cmake/
  ./docs/
  ./examples/
  ./grc/
  ./include/yourOOT/
  ./lib/
  ./python/
  ./swig/
CMakeFiles.txt
  The place to list dependences

## Slide 26: Build, Test, Install, Deploy, Reuse
Build
  $ mkdir ./build
  $ cd ./build
  $ cmake ../
  $ make
Test
  $ make test
Install
  $ make install

## Slide 27: Graphical part
GNURadio 3.8 forward
  YAML file describing
    Input and output ports
    Graphical appearance
    Construction arguments
    Documentation
GNURadio 3.7
  XML

## Slide 28: Outline
What is GNURadio
Building a block
Connecting Blocks
Packaging and deploying